## Slide 1: Image Processing
Fiammetta Caccavale

## Slide 2: Why working with images?
Images provide a visual cue for detecting many aspects that could affect processes, so they could be useful for
problems diagnostics
corrective actions

## Slide 3: Image Fundamentals - The Pixel Grid
Digital Image: A two-dimensional array (matrix) of numbers.
Pixels (Picture Elements): Each number in the array represents the intensity (brightness and/or color) at a specific location.

## Slide 4: Image Fundamentals - The Pixel Grid
Grayscale Images:
  One channel (typically 8-bit).
  Intensity values range from 0 (Black) to 255 (White).
Color Images (RGB):
  Three independent channels: Red, Green, and Blue.
  Each pixel has three values (one for each channel) to define its color.
Notes: # image from: https://www.google.com/search?q=yeast+images&tbm=isch&ved=2ahUKEwjUz-X_ldWCAxXcyAIHHYbhA1oQ2-cCegQIABAA&oq=yeast+images&gs_lcp=CgNpbWcQAzIFCAAQgAQyBQgAEIAEMgUIABCABDIFCAAQgAQyBQgAEIAEMgUIABCABDIGCAAQBRAeMgYIABAFEB4yBggAEAUQHjIGCAAQBRAeOgQIIxAnOgoIABCABBCKBRBDUNAJWIcYYLYaaABwAHgAgAFiiAHuCJIBAjEzmAEAoAEBqgELZ3dzLXdpei1pbWfAAQE&sclient=img&ei=FK1cZdT1C9yRi-gPhsOP0AU&bih=963&biw=1920&rlz=1C1GCEA_enDK978DK978#imgrc=6qAuQC86zVkngM

## Slide 5: Foundational Operations - Spatial Domain
Spatial Domain: Directly manipulating the pixel values of the image.
Point Processing (Pixel-wise):
  Operations applied to individual pixels, independent of neighbors.
  Examples: Contrast stretching, brightness adjustment, thresholding (converting to pure black/white).
Neighbourhood Processing (Filtering/Convolution):
  Operations applied to a pixel based on the values of its surrounding neighbours (the kernel/mask).
  Used for: Smoothing, Sharpening, and Edge Detection.

## Slide 6: Filtering: Smoothing and Sharpening
Smoothing Filters (Low-pass):
  Goal: Reduce noise and blur fine details (e.g., Gaussian Blur, Mean Filter).
  Mechanism: Averages the pixel values in the neighbourhood.
Sharpening Filters (High-pass):
  Goal: Enhance fine details and edges.
  Mechanism: Highlights intensity differences between a pixel and its neighbours.
Edge Detection:
  A specialized high-pass technique (e.g., Sobel, Canny).
  Identifies abrupt changes in image intensity, outlining objects.

## Slide 7: Real-World Applications
Computer Vision: Object recognition, facial recognition, autonomous vehicle navigation.
Medical Imaging: Enhancing X-rays, MRIs, and CT scans; detecting tumors or anomalies.
Remote Sensing: Satellite imaging for land-use classification, weather forecasting, and environmental monitoring.
Security and Surveillance: Motion detection, tracking, license plate recognition.
Photography and Graphic Design: Digital restoration, special effects, compression (e.g., JPEG).
https://www.kaggle.com/code/bonhart/brain-mri-data-visualization-unet-fpn

## Slide 8: Images in Chemical Engineering
Granulation
Computational Fluid Dynamics (bubble detection, segmentation, shape reconstruction)
Wastewater research
Spectral analysis
Fluidized bed applications
Bacterial growth
https://www.reshapebiotech.com/
Yizhou Cui, Chengxiang Li, Wanli Zhang, Xiaoqi Ning, Xiaogang Shi, Jinsen Gao, Xingying Lan, A deep learning-based image processing method for bubble detection, segmentation, and shape reconstruction in high gas holdup sub-millimeter bubbly flows, Chemical Engineering Journal, Volume 449, 2022, 137859, ISSN 1385-8947, https://doi.org/10.1016/j.cej.2022.137859.

## Slide 9: Application in Chemical Engineering
Particle Characterization:
  Quantifying particle size distribution, shape, and agglomeration in processes like crystallization and precipitation.
  Enables precise control over product quality and reaction kinetics.
Fluid Dynamics & Mixing Analysis:
  Analyzes complex flow fields, mixing efficiency, and turbulence in reactors and pipes.
  Tracks tracer particles to map velocity vectors.
Quality Control & Surface Inspection:
  Automated visual inspection of materials (e.g., coatings, membranes) for defects.
  Ensures consistency in manufacturing processes.
Reactor and Combustion Monitoring:
  Real-time observation of reaction zones, bubble size/velocity in fluidized beds, and flame analysis in furnaces.
  Provides data for optimizing reaction conditions and safety.

## Slide 10: What features can you extract from images?
Features you CAN’T extract from images:
pH
Concentrations
Features you CAN extract from images:
Particle size (effecting the transfer)
Shape (roundness, area)
Distance between particles
Infections

## Slide 11: Methods used
https://medium.com/@draj0718/convolutional-neural-networks-cnn-architectures-explained-716fb197b243
Modern image processing leverages ML, especially Convolutional Neural Networks (CNNs), for automatic feature extraction and advanced interpretation.

## Slide 12: Neural Networks
https://medium.datadriveninvestor.com/a-primer-into-neural-networks-a0bc02d8513b
https://regulaforensics.com/blog/neural-networks/
Biological Neuron
Artificial Neural Network

## Slide 13: Tutorials
Image processing material and exercise at:
https://github.com/FiammettaC/AI-for-Chemical-Engineers/tree/main/week05